## Slide 1
L78
0.33 uF
0.1 uF
5 V
12V
GND
12V
GND
3V3
JST
ERNI
ERNI
12 V battery
12V
GND
Logic Board
VT_2-
VT_2+
VT_1-
VT_1+
JST
Additional GPIO
5 V
GND
ADC
ERNI
Logic To Power
JST
RS485 -
RS485 +
GND
5 V
Pressure sensor
Air pump
Air valve
MasterMode switch
3V3
3V3
GND
GND
5 V
ERNI
12V
GND
1K

## Slide 2
Power Supply |  | 
1 | Battery 12 V | 
1 | Voltage Regulator 12 5V (L7805CV) | https://mou.sr/44wnume
1 | Capacitor 0.33 uF | 
1 | Capacitor 0.1 uF | 
1 | Voltage Regulator 12 3.3V (D24V22F3) | https://www.pololu.com/product/2857
Vibrotactile |  | 
2 | Audio Amplifiers (Mini-Haptuamp) | https://tactilelabs.com/products/mini-haptuamp/
2 | Sound exciters (check Zout compatibility with amplifier) (DAEX13CT-4 ) | https://www.daytonaudio.com/product/1172/daex13ct-4-coin-type-13mm-exciter-3w-4-ohm
Air chamber |  | 
1 | Optoisolator C226S | https://mou.sr/3QxHXBm
1 | Resistor 560 ohm | 
2 | Diodes 1N4007 | https://mou.sr/3UQq6YT
1 | Transistor BD911 | https://mou.sr/3ydirer
1 | Resistor 90 ohm | 
1 | Capacitor 110 nF | 
1 | 5V Air Pump | https://us.rs-online.com/product/rs-pro/7026898/70647434/
1 | 3.3V Air Valve | 
1 | Pressure sensor (MPXH6400AC6U) | https://mou.sr/4dxhYUE
2 | Silicon air chambers | 
1 | Silicon tube for air flow | 
2 | Tube joints | 
General |  | 
1 | Logic Board | 
1 | Switch SPDT | https://uk.rs-online.com/web/p/slide-switches/7347334
1 | LED | 
1 | Resistor 1kohm | 
2 | sEMG electrodes (13E200 Ottobock) | https://shop.ottobock.us/c/Electrode/p/13E200~550
1 | Jst  EMG adapter | 
2 | Jst  ERNI_10pins adapter | 
1 | Jst  microUSB adapter | 
3 | ERNi male port | https://it.rs-online.com/web/p/strip-e-connettori-pcb/0247616?gb=s
 | Matrix boards for prototyping | https://it.rs-online.com/web/p/schede-a-matrice/1596322?cm_mmc=IT-PLA-DS3A-_-google-_-CSS_IT_IT_ePMax_high-_--_-1596322&matchtype=&&gad_source=1&gclid=Cj0KCQjwxeyxBhC7ARIsAC7dS3-f15lH__SCWnDj-Y84NC73Bas111zslvWFvuxUNG1JMpuK-fii24AaAuzqEALw_wcB&gclsrc=aw.ds
 | PCB connectors | https://mou.sr/3UP7Uie
 | cables |